## Slide 1
AI Smart Agriculture Node
Integrating Relays, Sensors, and Edge-AI Controller on STM32
Lalith
2410040140
Subrahmanyam
2410040108
Pavan
2400040224

## Slide 2
Farming Meets Climate Era
Introduction & Background
Water is becoming scarcer, weather patterns are less predictable, and skilled agricultural labor is thin on the ground. Precise, always-on environmental control is no longer optional.
Water Conservation: Irrigate strictly on evidence, not rigid timer schedules.
Climate Variability: Sense micro-climate shifts and react within seconds.
Labor Efficiency: Autonomous sensing nodes replace tedious manual checks.

## Slide 3
STM32 Edge Processing
Processes real-time streams from DHT and soil-moisture sensors directly on-device. Eliminates cloud round-trip latency in critical control loops, ensuring ultra-fast, robust decision-making.
2-Channel Actuator Control
Directly drives a 2-channel relay module to switch a cooling fan and high-capacity water pump ON/OFF dynamically based on local Edge-AI model inference.
Edge-AI Microcontroller

## Slide 4
No. | Component | Functional Role in System
01 | 2-Channel Relay | Switches fan and water pump power ON/OFF based on STM32 decisions — the muscle of the node.
02 | Cooling Fan | Regulates canopy temperature and airflow to prevent heat stress and fungal build-up.
03 | Water Pump | Delivers precisely-timed irrigation, triggered only when soil moisture drops below threshold.
04 | DHT Sensor | Reads ambient temperature and relative humidity, feeding the microclimate inference model.
05 | Soil Moisture Probe | Measures volumetric water content in the root zone — the primary irrigation trigger signal.
Hardware Components

## Slide 5
01. Collect
Sensors (DHT + Soil Moisture probe) sample microclimate data at 1 Hz frequency.
02. Infer
STM32 runs on-device Edge-AI model (threshold & trend analysis) every loop cycle.
03. Switch
STM32 signals 2-Channel Relay (Relay CH1 for Fan, Relay CH2 for Pump).
04. Actuate
Microclimate adjusted in real-time; telemetry data logged for analytics.
System Architecture

## Slide 6
Outlook & Future Scope
A Small Board. A Bigger Harvest.
STM32 turns off-the-shelf sensors and actuators into a self-governing agricultural node — enabling smarter irrigation, healthier crop yield, and minimal resource waste.
Prototype Refinement: Optimizing firmware, custom PCB layout, and IP67 weather-proof enclosure.
Field Testing: Extensive validation across diverse crop types and seasonal climate extremes.
Mesh Scaling: Deploying multi-node wireless mesh networks for full-farm coverage.

## Slide 7
Thank You!
Any Questions or Feedback?
IoT Embedded Systems Project • STM32 Edge-AI Node
2410040140
2410040108
2400040224

## Slide 8
https://images.stockcake.com/public/a/1/6/a1655247-3eea-4e09-96d9-fe5f0d8dd95f_medium/sunrise-over-fields-stockcake.jpg
Source: stockcake.com
https://images.stockcake.com/public/e/0/8/e08f086e-cad0-45a9-b1e0-b25ab8db7227_large/sprouting-plant-watered-stockcake.jpg
Source: stockcake.com
Image Sources